Input Device Framework - Technical
Derek Bankieris
ER7
This presentation is does not reflect the changes introduced with the Ouput class, but is otherwise correct.

---
Controller Base Classes
- Represents a simulation interface to a particular system
- Lists minimum set of data a device must provide to act as such a controller
- Abstract – does not implement any functionality

---
Single Controller
- Represents an individual (virtual) controller
- Implements base class contract
- Contains an “Input” for each element of the required data set
- Provides methods for setting/getting inputs

---
Single Controller
- Does not represent a physical device
- Represents a virtual device that fulfills a system control contract
- Does not contain actual inputs
- Contains pointers to inputs, which allows for arbitrary mapping to physical devices (which do contain actual inputs)
- (we'll get to inputs in a moment)

---
Composite Controller
- Collection of single controllers
- Composite design pattern eliminates distinction between one and many
- Allows multiple controllers to service a single interface

---
Input Layout Classes
- Represents the collection of inputs available on specific physical devices
- Does not specify how those inputs are populated with data
- Does not specify a communication medium

---
Input Device Base Class
- Abstract base class for all physical devices
- Declares methods that all devices must implement
- Performs some generic error checking

---
Communication Medium Classes
- Represents devices which communicate over a particular medium
- Contains data & methods specific to that medium and common to devices of that type
- Performs one-time set-up and tear-down operations

---
Physical Device Classes
- Represents a physical device
- Ties a particular button layout to a specific medium of communication
- Responsible for reading and decoding data from the device and populating the inputs

---
Single Input
- Represents a single dimension of a physical input
- Allows specification of minimum, maximum, and (optionally) neutral raw values
- Scales raw values to [-1, 1]

---
Single Input
- Binary inputs (buttons)
  - Raw values are 0 or 1
  - Processed values are -1 or 1, respectively
- N-ary inputs (DOF, sliders, 3-state switches)
  - Raw values take on a range
  - -1 corresponds to the minimum raw value
  - 1 corresponds to the maximum raw value
  - 0 corresponds to the “neutral” (not necessarily median) raw value

---
Composite Input
- Composite design pattern again
- Allows the combining of multiple inputs into a single entity
- Provides for additively or proportionally combining values (still restricts output to [-1, 1])

---
Tying It All Together –
Hierarchy Layers
- Simulation Interface Layer
  - Declares the inputs that the simulation requires for each control system
  - Insulates control system code from the details of physical controllers
- Hardware Interface Layer
  - Represents physical devices
  - Responsible for all aspects of communication with devices
- Input Abstraction Layer
  - Exposes physical inputs available on particular devices
  - Acts as the conduit through which virtual controllers are tied to physical devices

---
Simulation Interface Layer
- Consists of composite design patterns, one for each type of control system
- Only layer with which control system code should interact

---
Input Abstraction Layer
- Contains the Input composite design pattern and a class for each collection of inputs available on a specific physical device
- This abstraction allows an identical input layout to be shared by devices whose only difference is the communication medium

---
Hardware Interface Layer
- Contains the root class, a class for each type of communication medium, and a class for each specific physical device
- Specific device classes combine a communication medium with an input layout from the input abstraction layer

---
Data Flow
The critical element is the “value” field within the SingleInput class. This field is updated when InputDevice::update() is called, which causes the specific device instance to read from the device, decode the data, and update its various Inputs. This value is ultimately returned by FlightController::getRoll().

---
Wiring the Connections
But how does getRoll() know to call getValue() from the leftRightPivot Input of WingMan? Someone has to tell it!
SingleFlightController fc;
UsbWingMan wingMan;
fc.setRoll(
wingMan.leftRightPivot);
fc.setPitch(
wingMan.forwardBackwardPivot);
fc.setYaw(wingMan.twist);

---
Wiring the Connections
- Complete flexibility in interpreting device inputs
- Supports dynamic reassignment
- Mappings can be written in C++ (if unlikely to change) or Python (if you want to change axes from run to run)
- Controllers can provide pre-configured mappings via static factory methods (if we feel that's appropriate)

---
Creating Composite Inputs
Use two buttons to command one axis:
SingleFlightController fc;
UsbWingMan wingMan;
CompositeInput zInput;
zInput.addInput(wingMan.button4);
zInput.addInput(wingMan.button5);
wingMan.button5.invert = true;
fc.setZ(zInput);

---
Creating Composite Inputs
- Recall that all inputs return a value in [-1, 1]
- Buttons are either pressed (1) or not pressed (-1)
- The CompositeInput from the previous slide will return 1 when button4 is pressed, -1 when button5 is pressed, and 0 when neither is pressed
- The FlightController does not care (or need to know) whether we use a single n-ary input or a composite of binary inputs

---
Sharing Input Layouts
- Eliminates code replication
- Allows code (outside of the hardware interface layer) to generically handle any particular input layout irrespective of its communication medium

---
Providing Default Mappings Via Factory Methods
SingleFlightController* SingleFlightController::createInstance(WingMan& wingMan) {
    CompositeInput* x = new CompositeInput();
    x->addInput(wingMan.hatNorth);
    x->addInput(wingMan.hatSouth);
    wingMan.hatSouth.invert = true;
    CompositeInput* y = new CompositeInput();
    y->addInput(wingMan.hatWest);
    y->addInput(wingMan.hatEast);
    wingMan.hatEast.invert = true;
    CompositeInput* z = new CompositeInput();
    z->addInput(wingMan.button4);
    z->addInput(wingMan.button5);
    wingMan.button5.invert = true;
    return new SingleFlightController(wingMan.leftRightPivot,
      wingMan.forwardBackwardPivot, wingMan.twist, *x, *y, *z);
}
SingleFlightController* SingleFlightController::createInstance(SpaceNavigator& spaceNavigator) {
    return new SingleFlightController(
      spaceNavigator.leftRightPivot,
      spaceNavigator.forwardBackwardPivot,
      spaceNavigator.twist,
      spaceNavigator.forwardBackwardTranslation,
      spaceNavigator.leftRightTranslation,
      spaceNavigator.upDownTranslation);
}

---
Adding a New Device to the Hierarchy
- Create a new communication medium class if the device's communication medium is not already represented
- Create a new input layout class if the device's input layout is not already represented
- Create a new device class that inherits from the classes in the two previous steps
- Implement logic to read and decode data from the device and to update the inputs
- Provide default mappings by adding factory methods to the controller classes that this device will support, if desired

---
Adding a New Controller to the Hierarchy
- Determine the list of inputs that the control system requires
- Create a new composite design pattern that consists of the abstract base class {Name}Controller, the implementing class Single{Name}Controller, and the composite class Composite{Name}Controller by following the structure of the existing controllers
- Provide default mappings by adding factory methods for the input layouts that this controller will support, if required

---
An Example – RATS SIM_MMSEV
//S_define
CompositeFlightController compositeFlightController;
CompositeCameraController compositeCameraController;
std::vector<InputDevice*> inputDevices;
...
(“initialization”) openDevices();
(hardwareRate, “scheduled”) updateDevices();
(flightRate, “scheduled”) flightControlSystem.controlFlight(compositeFlightController);
(cameraRate, “scheduled”) cameraControlSystem.controlCamera(compositeCameraController);
...
void addDevice(InputDevice& inputDevice) {
  inputDevices.push_back(inputDevice);
}
void openDevices() {
  for (std::vector<InputDevice*>::iterator i = inputDevices.begin(); i != inputDevices.end(); ++i) {
    (*i)->open();
  }
}
void updateDevices() {
  for (std::vector<InputDevice*>::iterator i = inputDevices.begin(); i != inputDevices.end(); ++i) {
    (*i)->update();
  }
}

---
An Example – RATS SIM_MMSEV
#input.py (assumes simObject is the name of an instantiation of the class on the previous slide)
# Open device on CAN network 0
device0 = trick.CanIndustrialProducts(0)
device0.thisown = 0
simObject.addDevice(device0)
# Open device on CAN network 1
device1 = trick.CanIndustrialProducts(1)
device1.thisown = 0
simObject.addDevice(device1)
# Use factory methods to create FlightControllers with default mappings for the devices
flightController0 = trick.SingleFlightController.createInstance(device0)
flightController0.thisown = 0
flightController1 = trick.SingleFlightController.createInstance(device1)
flightController1.thisown = 0
# Add the flight controllers to the simulation composite flight controller
simObject.compositeFlightController.addFlightController(flightController0)
simObject.compositeFlightController.addFlightController(flightController1)
# Use factory methods to create CameraControllers with default mappings for the devices
cameraController0 = trick.SingleCameraController.createInstance(device0)
cameraController0.thisown = 0
cameraController1 = trick.SingleCameraController.createInstance(device1)
cameraController1.thisown = 0
# Add the Camera controllers to the simulation composite Camera controller
simObject.compositeCameraController.addCameraController(CameraController0)
simObject.compositeCameraController.addCameraController(CameraController1)

---
An Example – RATS SIM_MMSEV
// Flight control system code
void controlFlight(FlightController& flightController) {
  // get the commanded inputs
  double roll = flightController.getRoll();
  double pitch = flightController.getPitch();
  double yaw = flightController.getYaw();
  double x = flightController.getX();
  double y = flightController.getY();
  double z = flightController.getZ();
  // control logic code
  ...
}
// Camera control system code
void controlCamera(CameraController& cameraController) {
  // get the commanded inputs
  double pan = flightController.getPan();
  double tilt = flightController.getTilt();
  double spin = flightController.getSpin();
  double zoom = flightController.getZoom();
  // control logic code
  ...
}
The arguments to these functions are the CompositeFlightController and CompositeCameraController from the S_define.